## Slide 1: Reducing noise in RTs
Andrew Thornett
For BAA H-Line Group Meeting 7/7/2025

## Slide 2: Reducing noise in radio telescope systems
Reducing noise in a 1420 MHz radio telescope setup (i.e., for detecting the hydrogen line) involves addressing:
internal sources of interference.
external sources of interference.

## Slide 3: Antenna System Optimization
Use a High-Gain, Directional Antenna
A Yagi-Uda or a large horn antenna will reduce off-axis noise pickup.
Ensure correct polarization (usually linear for hydrogen line work).
Antenna Location
Mount the antenna far from buildings, power lines, Wi-Fi routers, and computers.
Use ferrite chokes on coaxial cables where they enter buildings to reduce common-mode noise pickup.

## Slide 4: Low-Noise Front-End Electronics
Install a Low-Noise Amplifier (LNA):
Place the LNA as close to the antenna feed point as possible.
Look for noise figures under 1 dB if possible.
Power the LNA using bias-T to avoid long DC lines.
Use Quality Coaxial Cable (Low Loss):
LMR-400, RG-223, or similar; avoid RG-58 at these frequencies.
Keep cable runs as short as possible.

## Slide 5: Receiver and Filtering
Use a Narrowband Filter
Bandpass filter centred on 1420 MHz (±10–20 MHz) before the receiver to reject out-of-band RFI (e.g., from cell towers or Wi-Fi).
High-Q cavity or SAW filters are excellent for this.
Shielding
Shield the receiver (and computer if nearby) in a grounded metal box.
Use shielded cables for all digital connections.

## Slide 6: Eliminate Local Interference
Check for Internal RFI Sources
Switch off power supplies, monitors, or network devices near the antenna.
Use battery power or linear PSUs if possible for critical electronics.
Use a Faraday Cage (Optional but Powerful)
Shield your computer and SDR receiver in a fine-mesh grounded enclosure to trap radiated digital noise.

## Slide 7: Data Acquisition Techniques
Averaging and Integration
Stack multiple scans to increase signal-to-noise ratio (SNR).
Use software averaging over time and frequency bins.
Use a Clean Power Supply
Ensure your LNA and receiver get clean, regulated power. Switching noise from cheap PSUs can dominate your baseline.

## Slide 8: Environmental and Spectral Checks
Check Local RFI Spectrum
Use an SDR to scan from 1–2 GHz and identify any strong RFI sources near 1420 MHz.
Look for periodic signals (from switching supplies or clocked electronics).
Observe at Quiet Times
Nighttime and early morning often have lower RFI.
Avoid times when nearby devices like routers or street lights are active.