## Slide 1: Calculating Cantenna Dimensions for H-Line

## Slide 2: Astropeiler Stove-Pipe Cantenna Design

## Slide 3: Waveguide wavelength (λg) & probe placement — practical starting points
Waveguide wavelength λg = λ₀ / sqrt(1−(fc/f)²). Using the TE11 fc above:
145 mm dia → λg ≈ 404 mm → place probe ≈ 0.25–0.40·λg ≈ 100–162 mm from back wall as a tuning range to try.
165 mm dia → λg ≈ 319 mm → place probe ≈ 0.25–0.40·λg ≈ 80–128 mm from back wall. Many builders report good starting probe positions around 3–3.5 in (≈75–89 mm) for the ~154 mm cans; so use the ranges above and fine-tune while measuring return loss.

## Slide 4: Can length, probe tip and other tips
Can length: many practical designs use ~0.75–1.0·λg (experimentally people report ~0.75·λg works well for 6" cans). A short choke / flange at the mouth helps control pattern and improve matching.
Probe (pin) length: start near a quarter-wave in free space (~52–53 mm) and trim for best return loss inside the can. Use an LNA at the probe and an analyzer/SWR meter or NWA to tune.
Mechanical: 165 mm cans (or buckets) are a bit heavier/larger — make sure mounts and supports are solid. Add a choke/flange or taper if you use the cantenna as a feed for a dish.

## Slide 5: Mode behaviour for a 160 mm diameter cantenna
If D = 160 mm, c = 3e8 m/s, f = 1420.4058 MHz, λ0 ≈ 211 mm (free-space wavelength)
TE11 cutoff frequency
Formula (circular waveguide): fc_TE11 = (1.841 * c) / (pi * D)
Insert numbers (convert D = 0.160 m): fc_TE11 ≈ (1.841 * 3e8) / (3.1416 * 0.160)
fc_TE11 ≈ 1.10 GHz
TE21 cutoff frequency
fc_TE21 = (3.054 * c) / (pi * D)
Numerically:
fc_TE21 ≈ (3.054 * 3e8) / (3.1416 * 0.160)
fc_TE21 ≈ 1.82 GHz
Since: fc_TE11 < 1420 MHz < fc_TE21 the can operates single-mode at 1420 MHz (ideal).

## Slide 6: Waveguide wavelength (λg)
Formula:
λg = λ0 / sqrt(1 - (fc_TE11 / f)^2)
Compute ratio:
(fc_TE11 / f) ≈ (1.10 / 1.420) ≈ 0.775
(fc_TE11 / f)^2 ≈ 0.6006
Then:
1 - 0.6006 = 0.3994
sqrt(0.3994) ≈ 0.632
 λg = 211 mm / 0.632 ≈ 336 mm

## Slide 7: Probe distance from back of can
Use 0.25–0.40 of λg:
0.25 * λg ≈ 0.25 * 336 ≈ 84 mm
0.35 * λg ≈ 0.35 * 336 ≈ 118 mm
Recommended starting value:
Probe distance = 90–100 mm from the back plate

## Slide 8: Probe (feed pin) length
Start with quarter-wave in free space:
L_probe ≈ λ0 / 4
L_probe ≈ 211 / 4
L_probe ≈ 52–53 mm
Trim by a few mm during tuning.

## Slide 9: Summary Values
D = 150-160 mm
Height = 165 mm (good)
fc_TE11 ≈ 1.10 GHz
fc_TE21 ≈ 1.82 GHz
Operates single-mode at 1420 MHz
λg ≈ 336 mm
Probe distance = 90–100 mm, Astropeiler 93mm with D=150mm
Probe length = 52–53 mm

## Slide 10: Choke rings for cantennas in hydrogen line radio astronomy
A waveguide choke ring is a special conductive groove or structure around a waveguide opening, used to improve performance by suppressing unwanted modes, reducing reflections (improving impedance matching), or shaping radiation patterns, often seen in high-performance feeds for satellite dishes or specialized antennas to improve efficiency, bandwidth, and reduce cross-polarization. Essentially, it acts as a parasitic element or a broadband matching network to control how microwave energy radiates or couples between components, preventing signal leakage and improving directivity, especially in compact designs.

## Slide 12: Choke Ring Design (Waveguide Choke)
Choke ring = physical structure around mouth of cantenna/feed horn/antenna.
Purpose: Improves beam efficiency & reduces side lobes (cutting down noise from unwanted directions).
Design Considerations:
  Dimensions frequency-dependent: Dimeter & depth of choke ring is critical and precisely calculated based on operating frequency (1420 MHz for h-line projects).
  Calculation Tools: Specialized Excel sheets & software from sources like the SETI League or specific amateur radio operators (e.g., JA6XKQ) are used to determine these exact dimensions.
  Construction: Prototypes can be built from sheet metal or even simple folded mesh to test effectiveness.
  Placement: The choke ring is typically placed a short distance from the mouth of the feed element.

## Slide 13: SETI League Choke Design http://setileague.org/hardware/feedchok.htm
SETI League Photo

## Slide 14: Design by Barry Malowanchuk VE4MA

## Slide 15: Design by Barry Malowanchuk VE4MA

## Slide 16: Dual feedhorns installed on EA3UM 5m SETI dish. These cylindrical waveguide feedhorns utilize choke rings of VE4MA design. H-line feed offset from centre, allowing parasitic SETI whilst dish still used for another purpose.

## Slide 17: Argus Station Measurements https://www.seti.net/indepth/calculators/calculators.php

## Slide 18: SETI Calculators https://www.setileague.org/software/spreadsh.htm